## Slide 1: Carbon Capture And Storage Using Two Stage Aqueous Mineral Carbonation

## Slide 2: Supervisor: Dr. Imran Rashid Group Members Waleed Akbar (2018-CH-253) M. Shaiq Gohar (2018-CH-245) Sarmad Hashmi (2018-CH-275)
Department of chemical polymers and composite material engineering

## Slide 3: Contents
Introduction
Process Selection
Raw Material Selection
Process Flow Diagram and PFD description
Capacity Selection
Material and Energy Balance
Project Selection

## Slide 4: Introduction
CO2 is the most important greenhouse gas. Green house gasses are the one which absorbs and emit radiant energy within the thermal infrared range. So their excessive amount in atmosphere is dangerous
Carbon sequestration is the long-term removal, capture or sequestration of carbon dioxide from the atmosphere to slow or reverse atmospheric CO2 pollution and to mitigate or reverse global warming

## Slide 5: Project selection

## Slide 6: Why we select this project
By 2050, global population will rise from
&
the World enter demand is expected to increase by 50% over the next 20 years.
According to the recent Panel on Climate Change, global greenhouse gas (GHG) emissions must be reduced by 50 to 80 percent to avoid dramatic consequences of global warming.

## Slide 7: International Energy Agency, 2009
To avoid emission of CO2 in atmosphere we chose this

## Slide 8: Process selection

## Slide 9: We choose double stage carbonation

## Slide 10: Raw material selection

## Slide 11: We select Lizardite as raw material
Formula : Mg3(Si2O5)(OH)4
Color : green, brown, light yellow to white
Lustre : Resinous, Waxy, Greasy
Hardness:2½
Specific Gravity:2.55
Crystal System : Trigonal
Member of : Serpentine Subgroup

## Slide 12: Process flow diagram

## Slide 14: PFD description
Flue gases(CO2+N2) are coming from the plant that has temp. of 120C. These gases send to cooler where temp. reduces to 50C at atmospheric pressure.
Then these flue gases send to adsorber where the N2 is extracted and it converts rich amines into lean amines. The rich amines are made in the stripper where lean amines stream is attached and stripper makes amines rich that transfer to adsorber where N2 is extracted. This process is continuous for extraction of N2 and streams b/w adsorber and stripper are transferred with the help of pumps.

## Slide 15: Conti….
After stripper stream(99%pure,CO2) is send to compressor. From where it is send to the carbonation reactor and precipitator. CO2 analyzer is installed that analyze CO2.
We prepare slurry in mixer by adding activated feed material (Lizardite) and distilled water. It is send to the heater with the help of pump where its temp. rises. So that it can send to the carbonation reaction.
In carbonation reactor, slurry is added at 45C with 5 bar pressure and CO2 from compressor is added. From reactor CO2 is send to treated gas holder by analyzing with the help of CO2 analyzer.

## Slide 16: Conti….
From Carbonation reactor , product is send to the filter where undesired solids are removed from the product. From filter product is send to precipitator with the help of pump. After reaction in reactor product temp. is 90C and pressure is 2 bar.
In precipitator , product is added and CO2 that is 99% pure from compressor is added. Temp. reduced to 40C and stream is send to filter. From filter circulated water and product is separated. Our product is Nesquehonite.

## Slide 17: Capacity selection

## Slide 18: Capacity is selected as
1kg of CO2 required 2 kg of lizardite
1 ton = 1000kg
1 ton CO2 captured per day = 1000kg / day
CO2 capture per hour = 1000/24 = 41.67kg/h
So, plant is designed to capture and store 41.67kg of CO2
1kg CO2 require = 2kg of lizardite
41.67kg/h CO2 require = 83.34kg/h lizardite

## Slide 19: Material Balance

## Slide 20: Raw materials required
We need 2% conc. Slurry for the reaction
2% lizardite (solids)
98% sol (water)

## Slide 21: Slurry preparation
Lizardite flow rate = 83.334kg/h
Total inlet flow rate = 83.334/0.02 = 4166.7kg/h
Composition of lizardite = 0.02
Composition of solution = 0.98
Flow rate of solution = 4166.7(98)/100 = 4083.366kg/h

## Slide 22: Balance for slurry

## Slide 23: Adsorber Balance
2 streams are input in which one is rich amines and other is CO2
2 streams output 1 is lean amines and other is N2

## Slide 24: Stripper balance
1 stream is input that is lean amines
2 streams are out put 1 is rich mines and other is CO2

## Slide 25: Reactor balance
F+G=H+I
4166.7+86.57 = H+I
H+I = 4253.27KG/H
Lizardite balance
FAo =83.334kg/h = 8333g/h
M.M of lizardite = 277.11g/mol
N=mass/M.M= 8333/277.11=300.72 gmol/hr
FA =Fao (1-XA) = 300.725(1-0.5) =150.362
X(dissolution) at 45C,5 bar 600rpm in one hour taken a 50%.

## Slide 26: Contin….
C2O Balance
FB = FB0 –FA0 Xa (b/a)
Lizardite and CO2 reaction
MgSiO2O5(OH)4 + 3CO2 3MgCO3 + 2SiO2 + H2O + 64KJ/mol
Fb0 = CO2 in feed/M.W of CO2 = 41667/44= 946.96 gmol/h
Fb =946.96-(300.725)(0.5)(5)
=195.14moles/h

## Slide 27: Contin….
MgCO3 Balance
Fc = Fco-FaoXa(c/a)
MgCO3 was not initially present. So, Fco=0
Fc=0+300.725(0.5)(3)
Fc=451.087moles/h
SiO2 Balance
Fd= Fdo-FaoXa(d/a)
Fdo=0
Fd=300.725(0.5)(2)
Fd=300.725moles/h

## Slide 28: Contin….
In product stream
Lizardite=150.3625moles/h(277.11g/moles)=41.66kg/h
CO2
195.14(44)= 8.58kg/h
MgCO3
451.0875(84)=37.89kg/h
SiO2
300.725(60)= 18.043kg/h
We apply CO2 balance assuming that CO2 removed from the reactor is 99% pure

## Slide 29: Contin….
0.99H=8.58
H=8.66kg/h
I=4244.61kg/h
Composition of the stream is
Lizardite= 41.66/4244.61=0.0098
MgCO3=37.89/4244.61=0.0089
SiO2=18.043/4244.61=0.0042
H2O=4146.98/4244.61=0.977

## Slide 30: Contin….
2 streams are input 1 is slurry and other is CO2
2 streams are output 1 is CO2 and other is Product(Nesquehonite)

## Slide 31: Overall Material Balance
2 streams are input 1 is CO2 and other is Slurry
3 streams are output N2,H2O and our product(nesquehonite)

## Slide 32: Energy Balance

## Slide 33: Overall energy balance
Streams similar to material

## Slide 34: Adsorber balance
Streams similar to material

## Slide 35: Stripper balance
Streams similar to material

## Slide 36: Heater balance
Streams similar to material

## Slide 37: Reactor balance
Streams similar to material

## Slide 38: The End